## Slide 1: Cyberspace and the Internet
Computer Literacy

## Slide 2: Cyberspace
The term cyberspace was initially introduced by William Gibson in his 1984 science fiction novel Neuromancer
“A consensual hallucination experienced daily by billions of legitimate operators, in every nation, by children being taught mathematical concepts... A graphic representation of data abstracted from the banks of every computer in the human system. Unthinkable complexity. Lines of light ranged in the nonspace of the mind, clusters and constellations of data. Like city lights, receding.” [an excerpt of Neuromancer]
Notes: www.digitalattackmap.com/
www.norse-corp.com/

## Slide 3: Definitions of Cyberspace
“The notional environment in which communication over computer networks occurs” [Oxford Dictionaries]
“Cyberspace is an interactive domain made up of digital networks that is used to store, modify and communicate information. It includes the internet, but also the other information systems that support our businesses, infrastructure and services.” [UK Cyber Security Strategy]
“The complex environment resulting from the interaction of people, software and services on the Internet by means of technology devices and networks connected to it, which does not exist in any physical form” [ISO/IEC Guidelines for cybersecurity]
Are cyberspace and internet equivalent?
Notes: www.digitalattackmap.com/
www.norse-corp.com/

## Slide 4: Internet
Started in the 1960s
U.S. Defense Advanced Research Projects Agency funded ARPANET (Advanced Research Projects Agency Network)
  Project for secure communication for military and scientific purposes
  Idea: globally interconnected system of computers
Internet
  Global network of networks
  Functions via several major hubs around the world, where they connect and are able to connect to other major hubs
  Uses internet protocol suite (TCP/IP) to link devices
  Platform to exchange information

## Slide 5: Intranet
Local or private restricted network within an organization
Uses the same technologies and communication standards as Internet
Typically, information can only be access by authorized persons of that organization
Notes: Intranet is basically closed internet with any enterprise. In simple terms, enterprise data that only exists and lives within its own private network falls in the category of intranet.

## Slide 6: How does the internet work?

## Slide 7: Internet Addresses
Each computer connected to the internet must have a unique address
Known as an IP address (IP stands for Internet Protocol)
Assigned a temporary one through your ISP (internet service provider) for duration of your session
In IPv4…
  Address is a 32-bit number
  Take the form: nnn.nnn.nnn.nnn where nnn is a number from 0-255.
    172.16.254.1
internet
Your computer
1.2.3.4
Another computer
5.6.7.8

## Slide 8: Protocol Stacks
Suppose you want to send a message, “Hello friend!” to computer 5.6.7.8.
The message must be
  translated from alphabetic text into electronic signals
  transmitted over the internet
  then translated back into alphabetic text.
This is accomplished through the use of a protocol stack
  Every computer needs one to communicate
  Usually built into the operating system
The protocol stack used on the internet is referred to as the TCP/IP protocol stack.

## Slide 9: TCP/IP Protocol Stack
Protocol Layer | Comments
Applications Protocol Layer | Protocols specific to applications (WWW, e-mail, FTP, etc)
Transmission Control Protocol Layer | Directs packets to specific application on a computer using a port number
Internet Protocol Layer | Directs packets to a specific computer
Hardware Layer | Converts binary packet data to network signals and back (network card, etc)
The protocol stack used on the internet
Consists of four layers of protocols
Referred to as TCP/IP because of two major communication protocols used

## Slide 10: TCP/IP Protocol Stack: Sending a Message
Message starts at the top of the protocol stack on your computer and works its way downward
Data are sent in small, manageable chunks known as packets.
  If message is too long, each stack layer may break it up into smaller chunks.
Your computer
1.2.3.4
Another computer
5.6.7.8
Applications
TCP
IP
Hardware
Applications
TCP
IP
Hardware
Internet
Send email, for example
Assign port #
Direct to computer 5.6.7.8
Convert packets to electronic signals
Convert electronic signals to packets
Strip routing data
Reassemble packets
Receive email

## Slide 11: Main components of Network Infrastructure
Host — computer that has two-way access to other computers:
  Receives requests
  Replies to those requests
Network service providers (NSPs)
  Maintain the Internet backbone—the main high-speed routes
  Supply ISPs with access to high-speed transmission lines
  Provide routers at network connection points
Network access points (NAPs)
  How NSPs are linked
  Allow data to start on one network then cross to another
Routers
  Specialized devices that connect networks, locate the best path of transmission, and ensure that data reaches its destination

## Slide 12: Abstract Network Infrastructure
Host
Host
NSP Backbone
Modem
Router
Modem
Host
Regional ISP
Regional ISP
NSP Backbone
NAP
Router
Router
Router

## Slide 13: Simplified Internet Infrastructure
NSP Backbone
Regional ISP
Regional ISP
NSP Backbone
NSP Backbone
Regional ISP
Regional ISP
NAP
NAP
NAP
NAP

## Slide 14
Internet Infrastructure (Routing Paths)
[The Opte Project]

## Slide 15: Accessing the Internet

## Slide 16: Internet Service Providers
Internet service providers (ISPs)
  Supply and sustain user connections to the Internet
  Maintain the hardware and software
  Protect their sites and networks from outside threats
Hot spots
  Public location that provides Internet access for wireless devices
Important terminology
  Bandwidth: quantity of data that can be transmitted through a medium in a given amount of time
    Downstream speed: speed of data towards end user
    Upstream speed: speed of data from user to internet

## Slide 17: Common Types of Internet Access
Dial-up access: very slow; uses the phone line
Digital subscriber line (DSL): high-speed connection through telephone network; doesn’t interrupt telephone
Cable access: high-speed connection using a cable modem on coaxial wiring originally developed for TV; not phone line
Satellite: high-speed connection using satellite modem and dish
Fiber-optic service: very high-speed connection; fiber-optic lines direct to the home

## Slide 18: Domain Names and Address Resolution
You want to access cs.kent.edu, but don’t know the IP address.
Domain Name Service (DNS), is a distributed database which keeps track of computer’s names and their corresponding IP addresses on the internet
When you go to a web address in your browser..
  it first connects to a DNS server to perform address resolution
  May be redirected to another DNS if that domain name was not found

## Slide 19: Internet Domains
hostname is the name of the host computer and is followed by one or more domains separated by periods
Example: host.subdomain.subdomain.domain
  cs.kent.edu
  en.wikipedia.org
Some of the many, many top-level domains
  .biz—Businesses
  .com—commercial organizations
  .info—Information services
  .gov—government entities